## Slide 1: KickSat Conops
Tentative… to be discussed during the meeting Tuesday 07/10/18

## Slide 2
Launch
Mothership drops off the ISS
Deploy Antennae
1) Check battery voltage.
2) Deploy Antennae.
Hold
Mothership waits
Actual Time: TBD
No Uplink received by the mothership for some abnormal amount of time TBD
Separation Mode
Uplink received by the Mothership
Initial Downlink
Transmit basic info to the GS (battery info)
Standby Mode
Gather Sensor Data
Low Frequency Chirps
Low power consumption
Uplink Received, Downlink requested
Downlink Mode
Gather Sensor Data
Sending information to GS
Data Transmission is complete
Data Transmission is complete
Sprite Deployment Conditions have been met
Sprite Deployment Mode
Check Battery Level
Burn Wire #1 Actuated by MCU #1
Check Battery Level
Burn Wire #2 actuated by MCU #2
Check Battery Level
Burn Wire #3 actuated by MCU #2
Check Battery Level
Wait for a good amount of time TBD
Repeat these steps (End of Life)
TODO: Verify we want to kill the mothership after deployment
Safe Mode:
Low frequency chirps (battery level)
No Sensor Data
Do not allow deployment
ON RESET/REBOOT:
1) Boot initialize
2) read config with error correction
3) decide which mode to start in based on config file
Exit on Uplink Signal,
Return to correct mode based on config files
Enter Safe Mode (from any other mode) due to:
Critical Battery Level
Bad GPS data